## Slide 1
RFID is a radio transponder carrying an ID (Identification) that can be read through radio frequency (RF) interfaces. These transponders are commonly known as RFID tags or simply tags. To assign an identity to an object, a tag is attached to the object. Data within the tag provides identification for the object. The object could be an entity in a manufacturing shop, goods in transit, item in a retail store, a vehicle in a parking lot, a pet, or a book in a library. Biologists had been using RFID for sometimeto track animals for the purpose of studying animal behavior and conservation. The earliest use of RFID was for tracking farm animals. A RFID system comprises different functional areas like: 1. Means of reading or interrogating the data in the tag.2. Mechanism to filter some of the data.3. Means to communicate the data in the tag with a host computer4. Means for updating or entering customized data into the tag.RFID tags are categorized on three basic criteria. These are based on frequency, application area and the power level.On Frequency: There are six basic frequencies on which RFID operates. These are 132.4 KHz,13.56 MHz, 433 MHz, 918 MHz, 2.4 GHz and 5.8 GHz. Low frequency (30 KHz to 500 KHz) systems have short reading ranges and lower system costs. Tags in this frequency range are slow in data transfer and suitable for slow-moving objects. They are most commonly used in security access, asset tracking and animal identification applications. High-frequency (850 MHz to 950 MHz and 2.4 GHz to 2.5 GHz) systems offer long read ranges and high data transfer speeds. High reading speed is required for fast moving objects like railway wagon tracking and identification of vehicles on freeways for automated toll collection. The higher the frequency the higher the data transfer rates.On Application: RFIDs are also grouped according to application and usage. Speed of the object and distance to read determines the type of tag to be used. RFID used for livestock will be different from the tag used in railroad. The significant advantage of all types of RFID systems is the contactless, nonline-of-sight nature of the technology. Tags can be read through a variety of substances such as snow, fog, paint, plastic, wall, container and other challenging conditions, where barcodes or other optical means of reading are not effective. RFID tags can also be read at high speeds. In these cases RFIDs can respond within 100 milliseconds. A RFID tag contains two segments of memory. One segment is a factory-set and used to uniquely

## Slide 2
identify a tag. The other segment is usable by the application. Application specific data can be written or stored in this portion of the tag. The read/write capability of a RFID system is an advantage in interactive applications such as work-in-process or maintenance tracking. Compared to the barcode, RFID is a costlier technology. However, RFID has become indispensable for a wide range of automated data collection and identification applications that would not be possible otherwise.• Power-based Grouping: RFIDS can be grouped into two types based on power requirements. These are active and passive tags. Passive tags are generally in low frequency range, whereas tags at higher frequency range can be either active or passive.Active RFID Tags: Active tags are powered by an internal battery and are typically read/write.The life of an active tag is limited by the life of the battery. The data within an active tag can be rewritten or modified. An active tag's memory can vary from a few bytes to IMB. The battery-supplied power of an active tag generally gives it a longer read range. The trade off is, greater the size greater the cost, and a limited operational life. Depending upon the battery type and temperatures, the life of such tags could be 10 years. Some active tags can also be smart and do not send their information all the time. In a typical read/write RFID system, a tag might give a machine a set of instructions, and the machine would then report its performance to the tag. This encoded data would then become part of the tagged part's history. This data can be details about the port of transit with dates.• Passive RFID Tags: Passive tags operate without a power source of its own. A passive tag obtains operating power from the reader's antenna. The data within a passive tag is read only and generally cannot be changed during operation. Passive tags are lighter, less expensive and offer a virtually unlimited operational lifetime. The trade off is that they have shorter read ranges than active tags and require a higher-powered reader. Passive tags contain data usually 32 to 128 bits long.RFID tags are of different shapes and sizes. Animal tracking tags are inserted beneath the skin and are as small as a pencil lead. Tags can be screw-shaped to identify trees or wooden logs. In stores, plastic tags are attached to merchandise and used as anti-theft devices. Heavy-duty large tags are used to track containers or heavy machinery.